## Slide 1
Introducing Dev-Friendly
Wireless with the Notecard!
Rob Lauer
Director of Developer Relations

## Slide 2
Ray Ozzie – CEO of Blues Wireless
Complexity kills. It sucks the life out of developers, it makes products difficult to plan, build, and test.

## Slide 3: Section Agenda
Intro to the Notecard and Blues Wireless
Lab: Hands-on Wireless IoT
Lab: Collect Sensor Data and Send to Cloud

## Slide 5
”Making wireless IoT easier for developers
and more affordable for all”

## Slide 6
🔒 Securing your data from device to cloud
🔋 Building zero-config low-power hardware
👩‍💻 Providing an unmatched developer experience
Easy for developers and affordable for all.

## Slide 7
Notecard
Low-power system-on-module
Global cellular/GPS or Wi-Fi
500MB cell data + 10 years service
JSON-based API
Python, Go, Arduino, C/C++
Cellular: NB-IoT, LTE-M, Cat-1

## Slide 8
Notecarrier
Dev boards for easy prototyping
Notecarrier for every scenario:
  AF – Feather-compatible socket
  A – Any MCU, onboard antennas
  B – Small form factor
  Pi – Raspberry Pi SBC

## Slide 9
Notehub
Route data to any cloud app
Manage fleets of devices
OTA MCU/Notecard firmware updates
Secure communications

## Slide 10
Request
{ "req": "card.location" }
Example: card.location API
Response
{
"status": "GPS updated (58 sec, 41dB SNR, 9 sats),
"mode": "periodic",
"lat": 42.577600,
"lon": -70.871340,
"time": 1598554399
}

## Slide 11
JSON
Python
C/C++
Arduino
Your MCU/SBC
Your Sensors
Your Language
{JSON}
req = {"req": "note.add"}
req["file"] = "sensors.qo"
req["body"] = {"temp": 72.22 }
req["sync"] = True
rsp = card.Transaction(req)
Cellular/Wi-Fi
Notecard
🔒📡️🔒
Blues Wireless
Notehub.io
{JSON}
Any Cloud
{
"file": "data.qo",
"temp": 27.3,
"when": 1644268443,
"lat": 42.11,
"lon": -88.32
"device": "dev:89347"
}
Outbound Communication (from MCU to Cloud)

## Slide 12
Your MCU/SBC
Your Sensors
Your Language
{JSON}
Cellular/Wi-Fi
Notecard
🔒📡️🔒
Blues Wireless
Notehub.io
{JSON}
Any Cloud
Inbound Communication (from Cloud to MCU)
JSON
Python
C/C++
Arduino
req = {"req": "note.get"}
req["file"] = "data.qi"
req["delete"] = True
rsp = card.Transaction(req)
{
"file": "data.qi",
"sample_freq": 5,
"notify": true
}

## Slide 13
hackster.io/blues-wireless

## Slide 14
Lab! 🔨
Chromium-based Browser
  (e.g. Chrome, Edge, Brave)
Micro USB Cable
The Hammer of Blues

## Slide 15
Lab! 🔨
Arduino IDE + STM32Cube
VS Code + PlatformIO
Small PlatformIO Clone sensor project Walk through code | Medium Arduino or PlatformIO Follow dev.blues.io tut Use pseudo sensor | Large Arduino or PlatformIO Follow dev.blues.io tut Add real sensors
bit.ly/blues-hammer